## Slide 2: Proxy-Arp considered harmful
2011-11-03
RIPE63 – EIX Working Group
Wolfgang Tremmel
Director Support
wolfgang.tremmel@de-cix.net

## Slide 3
Internet
80.81.192.0/22
80.81.194.A/22
80.81.195.B/22
80.81.194.C/22
80.81.192.D/22
80.81.193.E/22
Internet
Notes: DE-CIX network layout. DE-CIX uses 80.81.192.0/22 as network, once, quite some time ago it used 80.81.192.0
We see a couple of hosts here from all /24s within the network.
Their IP address is not really imporant, so A B C D E is used as the last part.
The third digit (192, 193, 194, 195) they are using *is* important

## Slide 4
Internet
80.81.192.0/22
Internet
80.81.192.0/23
80.81.192.0/23
80.81.192.0/23
80.81.194.A/22
80.81.195.B/22
80.81.194.C/22
80.81.192.D/22
80.81.193.E/22
Notes: Somebody now announced a part of the network (80.81.192.0/23) in global BGP
This is bad enough
Quite a number our customers did not have proper BGP ingress filters set and accepted the announcement

## Slide 5
Internet
80.81.192.0/22
Internet
Accepted:
80.81.192.0/23
80.81.192.0/23
Accepted:
80.81.192.0/23
blocked
80.81.194.A/22
80.81.195.B/22
80.81.194.C/22
80.81.192.D/22
80.81.193.E/22
Notes: Here we see two routers accepted the announcement, one had proper filters.
You should deny BGP routes for 80.81.192.0/22 and *all smaller subsets of it*
Those routers who have accepted the announcement, now have a more specific route to all hosts within 80.81.192.0/23 in their routing table.
This allone would disrupt any traffic from them to hosts within 80.81.192.0/23
It does not matter that 80.81.192.0/22 is directly connected – more specific wins.
Obviously this only works for host which are not within 80.81.192.0/23 itself (?)

## Slide 6
Internet
80.81.192.0/22
Internet
Accepted:
80.81.192.0/23
80.81.192.0/23
Accepted:
80.81.192.0/23
blocked
ARP-Request: Who has 80.81.193.1?
80.81.194.A/22
80.81.195.B/22
80.81.194.C/22
80.81.192.D/22
80.81.193.E/22
Notes: Now see what happens when a host sends an ARP request for anything within 80.81.192.0/23

## Slide 7
Internet
80.81.192.0/22
Internet
Accepted:
80.81.192.0/23
80.81.192.0/23
Accepted:
80.81.192.0/23
blocked
ARP-Request: Who has 80.81.193.1?
No proxy-arp
80.81.194.A/22
80.81.195.B/22
80.81.194.C/22
80.81.192.D/22
80.81.193.E/22
Notes: Routers without proxy arp are silent

## Slide 8
Internet
80.81.192.0/22
Internet
Accepted:
80.81.192.0/23
80.81.192.0/23
Accepted:
80.81.192.0/23
blocked
ARP-Request: Who has 80.81.193.1?
No proxy-arp
Send Traffic for 80.81.193.1 to me!
80.81.194.A/22
80.81.195.B/22
80.81.194.C/22
80.81.192.D/22
80.81.193.E/22
Notes: But routers with proxy-arp enabled want to be helpful:
Yes – I know where 80.81.192.1 is – I have a more specific route for this pointing to one of my interfaces.
And since I do proxy-arp I need to tell this to anybody asking it on the directly connected Ethernet

## Slide 9: Proxy-ARP: a history
RFC 1027: „ Using ARP to Implement Transparent Subnet Gateways”
  1987: A network with 100 hosts was considered large
  Repeaters were common
  Subnetting was „the new thing“
  Proxy-Arp was a solution for connecting networks in which hosts were not aware of subnetting
Proxy-Arp „on“ as default in Cisco IOS since version 9 at least
Do we still need this?
Notes: Send a plea to all router vendors to disable proxy arp? They would probably ignore us anyway…

## Slide 10: DE-CIX: Lessons learned
Before the incidend we only tested proxy-arp when new customers connected
Configuration changes went unnoticed
Now:
  We test all connected customers for proxy-arp every 10 minutes
  In case we find one:
    24/7 support gets a message
    Customer is notified
    Customer port gets shut down
    As soon customer confirmes he has turned off proxy-arp he gets re-enabled
Notes: As proxy-arep does not enable itself, the detected customer must have done something, also this is covered by our terms and conditions and by our SLA as the customers router with proxy-arp enabled is not in compliance wiht our technical requirements

## Slide 11
Thank you
Join DE-CIX now!
DE-CIX Competence Center
Lindleystrasse 12
60314 Frankfurt/Germany
Phone +49 69 1730 902 - 0
info@de-cix.net
DE-CIX Competence Center @ Kontorhaus Building
Frankfurt Osthafen (Docklands)